Status of injection facility for Novosibirsk SCT-Factory
Alexey Petrenko, BINP
2019 Joint Workshop on Future charm-tau Factory, Sep. 26, 2019, Moscow.
http://www.inp.nsk.su/~petrenko/c-tau/Injector/GeoViews.html
e- linac
e+ linac
Damping Ring
e+/e- linac

---
2.5 GeV electron linac
All calculations are performed in Еlegant.
e-injector:
8 MeV,
9 mm·mrad
http://www.inp.nsk.su/~petrenko/c-tau/Injector/e-linac/FODO/Twiss.html

---
2.5 GeV electron linac
60 MeV gain in
3 m long RF-structure:
e-injector:
8 MeV,
9 mm·mrad

---
Positron production system
Positron distribution after the solenoid (Pavel Martyshkin):
http://www.inp.nsk.su/~petrenko/c-tau/Injector/p-linac/Martyshkin/

---
Transition to quadrupole focusing
Particle tracking of the full distribution:

---
Losses during transition to quadrupole focusing:

---
Similar system at KEK
From Pavel Martyshkin’s presentation

---
Full 1.5 GeV e+ linac:
http://www.inp.nsk.su/~petrenko/c-tau/Injector/p-linac/FODO_and_e-p_sep/Track.html

---
Debuncher:
Four double bend achromates
60 MeV
RF-structure

---
Debuncher:
Four double bend achromates
3.8 nC
60 MeV
RF-structure
3.5 nC
3.5 nC

---
Damping ring (scaled down CLIC Pre-Damping Ring)
Damping times: τx = 7.2 ms, τs = 3.5 ms
Equilibrium emittance: εx = 6.3 nm (including IBS)
http://www.inp.nsk.su/~petrenko/c-tau/Injector/damping_ring/Twiss.html
Wigglers
Wigglers
TME cells
TME cells
Red line marks existing tunnel

---
Scaling down CLIC Pre-Damping Ring
Designed for 2.8 GeV
http://project-clic-cdr.web.cern.ch/project-CLIC-CDR/Drafts/Yannis_DR.pdf
Similar magnetic field but with 1.5 GeV e+ now:
Proportionally scale all elements
Existing tunnel
Remove several FODO-periods.

---
Damping ring optical functions
Tunes are just the first try:
Chromaticity is corrected to some positive value:
http://www.inp.nsk.su/~petrenko/c-tau/Injector/damping_ring/Twiss.html

---
Initial beam size at εx = 1500 nm, εy = 1300 nm and σ(Δp/p) = 0.01

---
Positron bunch capture into the damping ring
Surprisingly the capture is reasonably good even into completely non-optimized optics.
(+ to be checked with realistic field errors)
Turn

---
Summary
With 4.8 nC (3e10 e-), 2.5 GeV electron beam on target we get 5 nC e+ after the solenoid at 200 MeV, 3.5 nC before the damping ring and 3.0 nC e+ captured by the damping ring:
1.5 GeV e+
3 nC
5 nC, 200 MeV e+
5 nC, 2.5 GeV e-
With 3.0 nC (2e10) e+ per shot it will take 10 Hz linac to get the required 2e11 e+/sec. With 7 ms damping time we can have even faster linac, 20 Hz operation will give a factor of two safety margin.