## Slide 1
Схема позитронного источника

## Slide 2: Positron source

## Slide 3
Число позитронов после мишени(слева),
общее энерговыделение в мишени (справа)
Энергия электронов 2.5 GeV
Мишень W74Re26 (возможно Тантал)
Радиационная длина XO = 3.5 мм
Средняя мощность энерговыделения в мишени 2×100 W
число е- 5×1010
толщина мишени 4.5XO
частота повторения 25 Гц

## Slide 4
Плотность энерговыделения от одного сгустка электронов
Пороговая плотность энерговыделения в W74Re26 35J/g (SLAC)
Толщина мишени, мм
Радиус, мм
Плотность энерговыделения, J/g
Плотность энерговыделения оси , J/g
Область максимального энерговыделения (90%÷100%)
2.5÷4.5XO по глубине
0.3 мм по радиусу
σR≈1.2 мм

## Slide 5
Current profile is a half of sine with a pulse length of 25 µs
Gap between coil turns is 0.4 mm
Gap between coil and FC body is 1 mm
Turns size is 9.6x14 mm
Elliptical cylinder 120x180 mm
Total length is140 mm
Conical part length is 70 mm
Min cone diameter is 8 mm
Max cone diameter is 44 mm
Cone angle is ≈30 degrees
Cylindrical hole diameter is 70 mm
Coil has 13 turns
cτ Flux Concentrator (FC) computer model

## Slide 6
Elliptical cylinder 120x180 mm
Total length is140 mm
Conical part length is 70 mm
Min cone diameter is 8 mm
Max cone diameter is 44 mm
Cone angle is ≈30 degrees
Cylindrical hole diameter is 70 mm
Coil has 13 turns
Current profile is a half of sine with a pulse length of 25 µs
Gap between coil turns is 0.4 mm
Gap between coil and FC body is 1 mm
Turns size is 9.6x14 mm
Target rod (W74Re26) diameter is 4 mm, length is 15.7 mm
External target unit diameter is 35 mm

## Slide 7
Model 1.
Target position of end face
is -2mm
Model 2. Modification of FC front face around of a target
Model 3. Modification of gap between FC front face and target
Target position of end face is -1mm
0 position
Min cone diameter is 8 mm
Modifications of target position and FC front face

## Slide 8
Longitudinal magnetic field component on axis of Flux Concentrator. Peak field position is 3 mm
Transverse magnetic field components on axis of Flux Concentrator

## Slide 9
Peak field position is 8 mm
Cone angle is 30O
Cone angle modification with 23O and 45O
Transverse magnetic field components on axis of Flux Concentrator

## Slide 10
Elliptical cylinder 120x180 mm
Total length is140 mm
Conical part length is 70 mm
Min cone diameter is 8 mm
Max cone diameter is 44 mm
Cone angle is ≈29 degrees
Cylindrical hole diameter is 70 mm
Coil has 13 turns
Current profile is a half of sine with a pulse length of 25 µs
Peak current is ~ 20 kA (peak field is 7 Tesla)
Gap between coil turns is 0.4 mm
Gap between coil and FC body is 1 mm
Turns size is 9.6x14 mm
Target (W74Re26) diameter is 90 mm, thickness is 15.7 mm
Gap between target and FC front face is 2mm
FCC-ee FC Computer model with a positron production target

## Slide 11
Elliptical cylinder 120x180 mm
Total length is140 mm
Conical part length is 70 mm
Min cone diameter is 8 mm
Max cone diameter is 44 mm
Cone angle is ≈29 degrees
Cylindrical hole diameter is 70 mm
Coil has 13 turns
Current profile is a half of sine with a pulse length of 25 µs
Peak current is ~ 20 kA (peak field is 7 Tesla)
Gap between coil turns is 0.4 mm
Gap between coil and FC body is 1 mm
Turns size is 9.6x14 mm
Target (W74Re26) diameter is 90 mm, thickness is 15.7 mm
Gap between target and FC front face is 2mm
FCC-ee FC Computer model with a positron production target

## Slide 12
Model #1 grooving gap is 2 mm, gap between FC front face and target is 2 mm
Model #2 grooving gap is 2 mm, gap between FC front face and target is 3 mm
Model #3 grooving gap is 2 mm, gap between FC front face and target is 4 mm
Model #4 grooving gap is 3 mm, gap between FC front face and target is 4 mm
Model #5 grooving gap is 4 mm, gap between FC front face and target is 4 mm
Geometry Variations of
FCC-ee FC Computer model
‘0’ position

## Slide 13
Model #1 grooving gap is 2 mm, gap between FC front face and target is 2 mm
Model #2 grooving gap is 2 mm, gap between FC front face and target is 3 mm
Model #3 grooving gap is 2 mm, gap between FC front face and target is 4 mm
Model #4 grooving gap is 3 mm, gap between FC front face and target is 4 mm
Model #5 grooving gap is 4 mm, gap between FC front face and target is 4 mm
Field profiles on FC axis

## Slide 14
Энергия, MeV
Угол, градусы
Энергия, MeV
Угол, градусы
Энергетически-угловое распределение позитронов после мишени
Энергетически-угловое распределение позитронов после мишени (захват)

## Slide 15
Фазово-энергетическое распределение сгустка позитронов после соленоида
Поперечный размер e- (σ) 0.5 мм
Продольный размер e- (σ) 1.0 мм
Фазовая длина сгустка, градусы
Энергия, MeV

## Slide 16
Оценочный захват позитронов ( e+ энергия ~200 MeV после соленоида)
Диаметр структуры 24мм

## Slide 17
Оценочный захват позитронов ( e+ энергия ~200 MeV после соленоида)
Диаметр структуры 30мм

## Slide 18
Эмиттанс позитронного сгустка ( e+ энергия ~200 MeV после соленоида)
Эмиттанс не зависит от поля концентратора потока

## Slide 19
Размер позитронного сгустка (e+ энергия ~200MeV)
Поле концентратора 80 кГс
Поле соленоида 7 кГс
RMS размер ~ 4.1 mm
Горизонтальное смещение ~ 0.6 mm
Вертикальное смещение ~ 1.2 mm
X, мм
Y, мм

## Slide 20
 | FC–Solenoid field, Tesla |  |  |  |  | 
 | 8-0.6 |  | 8-0.7 |  | 8-0.8 | 
Acc. Structure diameter, mm | 24 | 30 | 24 | 30 | 24 | 30
Positron yield Ne+/Ne- | 0.6 | 0.76 | 0.69 | 0.83 | 0.76 | 0.88
Emittance, µm | 13.1 | 19.6 | 14.5 | 22.2 | 15.7 | 23.6
Vertical offset, mm | 1.1 | 1.2 | 1.2 | 1.2 | 1.1 | 1.25
Horizontal offset, mm | 0.76 | 0.7 | 0.6 | 0.8 | 0.6 | 0.7
Expected positron yield (e+ energy ~200MeV)
“Safety factor” of a positron system is about 2

## Slide 22: positron beam line